https://github.com/orgs/PacktPublishing/repositories?type=all Все исходники Packt

tail -f /var/log/kern.log сообщения ядра

# iptables --table nat --append POSTROUTING --out-interface eth1 -j MASQUERADE
# iptables --append FORWARD --in-interface eth4 -j ACCEPT
# echo 1 >> /proc/sys/net/ipv4/ip_forward

Then, for instance, on the BeagleBone Black I should set the gateway through the USB cable using the
following command:
root@bbb:~# route add default gw 192.168.7.1
 (eth1 device is the preferred Internet connection on my host system, while the eth4 device is the BeagleBone Black's device as viewed on my system )

apt-cache search gcc-[0-9.]*-arm показывает все компиляторы в репозитории
gcc-9-arm-linux-gnueabihf - GNU C compiler (cross compiler for armhf architecture)
gcc-9-arm-linux-gnueabihf-base - GCC, the GNU Compiler Collection (base package)
gcc-10-arm-linux-gnueabi - GNU C compiler (cross compiler for armel architecture)
gcc-10-arm-linux-gnueabi-base - GCC, the GNU Compiler Collection (base package)
gcc-10-arm-linux-gnueabihf - GNU C compiler (cross compiler for armhf architecture)
gcc-10-arm-linux-gnueabihf-base - GCC, the GNU Compiler Collection (base package)
gcc-8-arm-linux-gnueabi - GNU C compiler (cross compiler for armel architecture)
gcc-8-arm-linux-gnueabi-base - GCC, the GNU Compiler Collection (base package)
gcc-8-arm-linux-gnueabihf - GNU C compiler (cross compiler for armhf architecture)
gcc-8-arm-linux-gnueabihf-base - GCC, the GNU Compiler Collection (base package)
gcc-9-arm-linux-gnueabi - GNU C compiler (cross compiler for armel architecture)
gcc-9-arm-linux-gnueabi-base - GCC, the GNU Compiler Collection (base package)

( http://www.linaro.org/
https://releases.linaro.org/components/toolchain/binaries/ Перечень всех тулчейнов до версии 7

wget -c https://releases.linaro.org/components/toolchain/binaries/5.3-2016.02/arm-linux-gnueabihf/gcc-linaro-5.3-2016.02-x86_64_arm-linux-gnueabihf.tar.xz

tar xf gcc-linaro-5.3-2016.02-x86_64_arm-linux-gnueabihf.tar.xz

You can put your new toolchain whenever you wish inside the host's filesystem. We put it in the
/opt/linaro directory.

Then, we have to set up our environment in order to be able to execute the cross-compiler and other
components:
$ export PATH=/opt/Linaro/gcc-linaro-5.3-2016.02-x86_64_arm-linux-gnueabihf/bin/:$PATH

в ~/bashrc добавил:
export PATH=$PATH:/opt/Linaro/gcc-linaro-5.3-2016.02-x86_64_arm-linux-gnueabihf/bin/

Проверяем:
arm-linux-gnueabihf-gcc –version
arm-linux-gnueabihf-gcc (Linaro GCC 5.3-2016.02) 5.3.1 20160113
Copyright (C) 2015 Free Software Foundation, Inc.
This is free software; see the source for copying conditions. There is NO
warranty; not even for MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE.

minicom -o -D /dev/ttyUSB0
ls -l /dev/ttyUSB0

U-Boot (with MLO)

git clone https://github.com/u-boot/u-boot

$ cd u-boot
$ git checkout v2016.03 -b v2016.03 (Потребовалось вручную по тегу переключать)

wget -c https://rcn-ee.com/repos/git/u-boot-patches/v2016.03/0001-am335x_evm-uEnv.txt-bootz-n-fixes.patch
patch -p1 < 0001-am335x_evm-uEnv.txt-bootz-n-fixes.patch

patching file board/ti/am335x/board.c
patching file board/ti/am335x/board.h
patching file board/ti/am335x/mux.c
patching file common/spl/spl.c
patching file configs/am335x_evm_defconfig
patching file include/configs/am335x_evm.h
patching file include/configs/ti_armv7_common.h

Now, we're ready to compile. Let's do it with the following commands:
$ make ARCH=arm CROSS_COMPILE=arm-linux-gnueabihf- am335x_evm_defconfig
  HOSTCC scripts/basic/fixdep
  HOSTCC scripts/kconfig/conf.o
  SHIPPED scripts/kconfig/zconf.tab.c
  SHIPPED scripts/kconfig/zconf.lex.c
  SHIPPED scripts/kconfig/zconf.hash.c
  HOSTCC scripts/kconfig/zconf.tab.o
  HOSTLD scripts/kconfig/conf
#
# configuration written to .config
#

$ make ARCH=arm CROSS_COMPILE=arm-linux-gnueabihf-
Now, it's time to install the bootloader into the microSD
lsblk

sudo dd if=/dev/zero of=/dev/sdb bs=1M count=10
This is a very important step!
sudo dd if=MLO of=/dev/sdb count=1 seek=1 bs=128k
sudo dd if=u-boot.img of=/dev/sdb count=2 seek=1 bs=384k
Now, we can prepare the needed partition for the root filesystem, which will be installed in the
upcoming sections
echo '1M,,L,*' | sudo sfdisk /dev/sdb
sudo mkfs.ext4 -L rootfs /dev/sdb1

$ sudo mkdir /media/rootfs
$ sudo mount /dev/sdb1 /media/rootfs/
$ sudo mkdir -p /media/rootfs/opt/backup/uboot/
$ sudo cp MLO /media/rootfs/opt/backup/uboot/
$ sudo cp u-boot.img /media/rootfs/opt/backup/uboot/

Now, we have just to add U-Boot's environment commands to properly load the kernel. We have to
put all commands into a file called uEnv.txt in rootfs as follows:

$ sudo mkdir /media/rootfs/boot/
$ sudo cp ../uEnv.txt /media/rootfs/boot/ (файл изначально в GNU-Linux-Rapid-Embedded-Programming-master/Chapter01 )

Now, it's time to compile the kernel.
По книге непонятно – пробую ядро собрать по другим источникам
https://embedjournal.com/kernel-compilation-beaglebone-black/

Та же последовательность Источник тот-же Linaro (см выше)
Компилятор
sudo tar xvf gcc-linaro-arm-linux-gnueabihf-4.8-2014.04_linux.tar.xz -C /opt/
cd /opt/
sudo mv gcc-linaro-arm-linux-gnueabihf-4.8-2014.04_linux/ gcc-arm-linux
export PATH=$PATH:/opt/gcc-arm-linux/bin

U-boot
git clone git://git.denx.de/u-boot.git u-boot/
cd u-boot
$ git checkout v2016.03 -b v2016.03 (в мастере этого конфига уже нет поэтому возвращаемся на старую ветку)
make ARCH=arm CROSS_COMPILE=arm-linux-gnueabihf- am335x_boneblack_defconfig
make ARCH=arm CROSS_COMPILE=arm-linux-gnueabihf-

For deploying kernel from sd card, we need to format it and place the files accordingly. For this process, “Gparted” tool is needed. Install Gparted by the following command.
sudo apt-get install gparted
Insert your sd card by means of card reader and open Gparted. Select your sd card from the top right corner. it will be something like this, “/dev/sdb”
Note: Always use sd card of size greater than 2 GB. Although, 500 MB is more than enough for our task, having large free space will come handy at times.
Right click on the rectangular area showing your sd card name and select unmount as we need to unmount the existing partitions. Then, delete the existing partitions by again right clicking and selecting “delete”. This will delete all your files in sd card, so make sure you backed up any important files. We need two partitions in order to boot the kernel, one is for storing the bootable images and another one is for storing the minimal RFS(Root File System). Select new option by right clicking the partitions and provide the following details:
New size: 50MBembed journal
File System: FAT32
Label: BOOT
Click Add button. Then, create another partition for storing RFS by entering the options below
New Size: 1000MB
File System: EXT3
Label: RFS
Finally, click the green tick mark at the menu bar. The partition will be created and you can see two partitions created as BOOT and RFS.

Kernel
git clone https://github.com/beagleboard/linux.git

git checkout -b beaglebone-3.2
git checkout -b beaglev-v5.10.113-1.1.2
git checkout -b beaglev-v5.10.113-1.1.2-ubuntu

Before compiling the kernel we need to configure it. It will be hard for the newbies. Once again, thanks to the kernel developers for providing all configurations in a single file. Go to the kernel directory and issue the following command.

sudo apt-get install gcc-arm-linux-gnueabihf иначе на находился компилятор
sudo make ARCH=arm CROSS_COMPILE=arm-linux-gnueabihf- bb.org_defconfig такого файла нет
make ARCH=arm CROSS_COMPILE=arm-linux-gnueabihf- omap2plus_defconfig
#
# configuration written to .config
#
sudo make ARCH=arm CROSS_COMPILE=arm-linux-gnueabihf- uImage dtbs LOADADDR=0x80008000 -j4

не до конца - ошибки

sudo apt-get install u-boot-tools
  CALL scripts/checksyscalls.sh
  Kernel: arch/arm/boot/Image is ready
  Kernel: arch/arm/boot/zImage is ready
  UIMAGE arch/arm/boot/uImage
Image Name: Linux-6.8.0-rc7
Created: Fri Mar 15 13:05:49 2024
Image Type: ARM Linux Kernel Image (uncompressed)
Data Size: 5221248 Bytes = 5098.88 KiB = 4.98 MiB
Load Address: 80008000
Entry Point: 80008000
  Kernel: arch/arm/boot/uImage is ready

After compiling you can find the image files in “arch/arm/boot/” directory. Copy “uImage” file from this directory and also “am335x-boneblack.dtb” file from “arch/arm/boot/dts/” directory to the BOOT partition.

Нет файла dtb
Есть директория DTS нужно скомпилировать файл